## Slide 1
An Open Python Framework for Battery Operational Reliability Estimation
With Quantitative Minimum-Data Guidelines from a Synthetic Scaling Study
Team Dynamic • June 2026
2–50
Synthetic cells
0.97
AUC at N=8
0.46
Real-data AUC
3
Code bugs fixed

## Slide 2
Why this matters
Grid batteries face a critical decision: accept or reject each service request.
✅ Say yes when healthy → earn revenue
❌ Say yes when failing → blackout, penalties
❌ Say no when fine → lost revenue
Shikdar & Laaksonen (2026) built an ML framework to predict failure probability across 10–50 cycle horizons.
Reported AUC = 0.944 on 37 batteries
Failure rate reduction: 10.3% → 2.95%
Can we reproduce this with the 4-cell NASA dataset?

## Slide 3
Our Reproducibility Pipeline
Data layer: NASALoader parses .mat files → normalized DataFrame with SOH, voltage, current, temperature features
Model layer: XGBoost multi-output classifier per horizon, isotonic calibration on held-out validation fold
Dispatch layer: Threshold policies, continuous derating, Monte Carlo market simulator (AR(1) price model)
Evaluation: Leave-one-battery-out CV, AUC/Brier/ECE metrics, per-fold variance reporting
Run with: python run_all.py --quick (completes in < 10 seconds)

## Slide 4
The NASA 4-Cell Dataset
B0005
168 cycles, min SOH=0.699
B0006
168 cycles, min SOH=0.572
B0007
168 cycles, min SOH=0.744
B0018
132 cycles, min SOH=0.729
Key limitation:
Only 64 cycles fall below the EOL threshold (SOH < 0.70)
62 of those come from a single cell (B0006)
Leave-battery-out CV: train on 3 cells, test on 1
Most folds have zero positive samples → AUC cannot be computed

## Slide 5
Results: Near-Random Discrimination
Horizon | Raw AUC | Calibrated AUC | Per-fold (mean±std)
H=10 | 0.26 | 0.50 | — (2/4 folds NaN)
H=20 | 0.26 | 0.50 | — (2/4 folds NaN)
H=30 | 0.60 | 0.50 | 0.50±0.00
H=50 | 0.69 | 0.50 | 0.50±0.00
Macro avg | 0.46 | 0.50 | 0.50±0.00
Random guessing = AUC 0.50. The raw model produces near-constant predictions (no rank variation). Isotonic regression preserves rank order — with no rank order to preserve, AUC is undefined and conventionally reported as 0.5.
Original paper achieved AUC 0.944 on 37 batteries — the framework needs substantial data.

## Slide 6
Synthetic Scaling Study: AUC vs Dataset Size
For N in {2, 3, 5, 8, 12, 20, 30, 50} with 3 Monte Carlo seeds each:
N cells | Mean AUC | ±1 Std | Regime
2 | 0.84 | 0.009 | Insufficient
3 | 0.90 | 0.019 | Insufficient
5 | 0.93 | 0.007 | Insufficient
8 | 0.97 | 0.002 | Marginal
12 | 0.98 | 0.002 | Reliable
20 | 0.99 | 0.001 | Reliable
30 | 0.99 | 0.001 | Reliable
50 | 0.99 | 0.001 | Reliable
Diminishing returns beyond N=8–12. Real-world data will need more (est. 15–25 for AUC > 0.95).
Per-horizon breakdown (representative seed): N=3 → H=10:0.88, H=20:0.89, H=30:0.91, H=50:0.92 — all horizons improve together.
Diversity caveat: Synthetic data maximizes cell diversity. Real batteries share chemistry/manufacturer — correlated degradation reduces effective diversity.
Variance note: N ≤ 3 estimates based on 2–3 CV folds, interpret cautiously. | Comput. cost: full scaling ~2–3 h, NASA real-data < 10 s.

## Slide 7
Three Hidden Bugs We Found
Bug 1: Calibration Data Leakage
Original code fit the isotonic calibrator on test data — then evaluated on that same data. This inflated AUC from 0.46 to an apparent 0.74. Fix: fit on a held-out validation fold.
Bug 2: Energy Unit Confusion
Revenue = energy (kWh) × price ($/MWh) — without dividing by 1000, revenue was overstated by 1000× ($3,780 vs $3.78).
Bug 3: Inconsistent Baseline Metric
Baseline failure rate used label density across all horizons; model rows used conditional dispatch-based metric. These are incomparable.

## Slide 8
Ablation Study
Configuration | Failure Rate | Energy
Always dispatch | 0.0063 | 318.0
+ Raw hazard model | 0.0063 | 318.0
+ Probability calibration | 0.0063 | 318.0
+ Composite failure labels | 0.0110 | 318.0
Composite labels increase the failure rate — the NASA dataset lacks resistance measurements, so composite labels add noise without predictive signal.

## Slide 9
Key Takeaways
First quantitative scaling curve for battery ML
AUC vs N: N ≤ 5 = insufficient, 5 < N < 12 = marginal, N ≥ 12 = reliable. Real data estimated at 15–25+ for AUC > 0.95.
Open-source framework with correct methodology
Three bugs documented and fixed: calibration leakage (+0.28 AUC), energy unit error (1000×), inconsistent baselines. All code public.
Honest real-data validation
On 4 NASA cells, AUC = 0.46 — confirming the framework needs more data than one public benchmark. Anyone can reproduce.

## Slide 10
Our Python Package
Modular — data, models, dispatch, evaluation layers
Correct calibration — fit on validation fold, not test set
Unit-aware economics — correct kWh ↔ $/MWh conversion
Consistent metrics — same dispatch-based metric for all ablation rows
Scaling experiment — --expt scaling runs N=2..50 Monte Carlo study
Synthetic data fallback — pipeline runs without external files
Full configuration — single config.yaml controls everything
Code: github.com/teamdynamic/battery-reliability-extension
DOI: 10.5281/zenodo.15089441

## Slide 11
Limitations & Future Work
Current limitations
Only 4 cells, all 18,650 format under lab conditions
No deep learning (LSTM, TCN, Transformer) — CPU constraints
Simplified AR(1) price model
CALCE cross-chemistry evaluation incomplete
Future work
Evaluate on larger public datasets (10+ batteries)
Cross-chemistry validation (LFP, NMC)
GPU-based deep learning benchmarks
Real price data instead of AR(1) simulation

## Slide 12
Thank You
Questions? Feedback?
Paper: Extension_Paper.docx
Code: github.com/teamdynamic/battery-reliability-extension
Team Dynamic • June 2026